| Firmware-Versionen |
| --- |
| Ver. | EPROMs | ab SN-Nr./ Jahr | AT=Autotune, ED=Edit, CI=Cass.-Interface |
| 1 | AB0/A1/A2 | 810101 Jan 81 | 32 Prgs, altes AT, altes ED |
| 2 | AD0/A1/A2 | 810201 Jan 81 | 32 Prgs, altes AT, altes CI, neues ED |
| 3 | B0/BA1/BA2 | 813701 Sep 81 | 120 Prgs, altes AT, neues CI, neues ED, zusätzliche Speicherplatine |
| 4 | C0/C1/C2 | 814203 Okt 81 | 120 Prgs, neues AT mit Auto-Disable, altes CI, neues ED |
| 5 | C0/CA1/C2 | 814401 Nov 81 | 120 Prgs, neues AT, neues CI, neues ED (produz. bis Feb 82) |
| 6 | F0/F1 | 814701 Nov 81 | 120 Prgs, neues AT, neues CI, neues ED, Prozessor-Board |
| 7 | FA0/F1 | 820301 Jan 82 | wie vor, software-noise-Fix |
| 8 | G0/G1 | 820818 Feb 82 | wie vor, digitales Portamento |
| 9 | GA0/G1 | 820901 Feb 82 | wie vor, edit-doubling-fix |

XACA2:

The reason for this is that the autotune acceptance range in the original OS is +0 / -24 cents. In other words, it's acceptable for an oscillator to be 24 cents flat, but not a single cent sharp. This is obviously a bug, as the acceptance range should be symmetric. I therefore modified the autotune acceptance range to be +/- 6 cents. It would be quite easy to change this to +/- 12 cents if necessary to get the same acceptance range as the original but without the offset, but if the synthesizer is working properly it should be no problem to get the oscillators within +/- 6 cents; it should be much closer than that anyway.

the revised XAC2.BIN EPROM for the the OB-Xa, file name XACA2.BIN (checksum B559h if you want to verify the downloaded image). If you want to try this, but you don't have an XAC2.BIN EPROM in your OB-Xa but rather another firmware version, email me and I'll send you images for the whole set.